## Slide 1: An Open-source Discrete Element Knee Model
Anne Schmitz

## Slide 2: Main Model Components
Joints
6 DoF tibiofemoral
1 DoF patellofemoral
18 ligament bundles
ACL (2), PCL (2), MCL (5), LCL (1), PFL (1), posterior capsule (4), patellar tendon (3)
Positioned using anatomical landmarks
Modeled as nonlinear springs with properties from literature (modeling and tensile testing)
Articular contact geometry
Femur cartilage from MRI (OpenKnee)
Tibial plateaus as planes (also used by other knee models like this)
Each compartment modeled separately so contact forces are resolved into medial and lateral sides
Contact
Linear elastic foundation model contact between bones (as used by other models)
Contact between MCL and femur to avoid penetration

## Slide 3: Segment Coordinate Systems
Bone embedded reference adapted from (Arnold, et al., 2010)
In anatomical position, x‐axis pointed anteriorly, y‐axis superiorly, and the z‐axis to the right.
Aligned with the inertial axes of each bone.
Femur
  Origin at center of the femoral head
  Y‐axis placed along a line connecting the femoral head and the center of the femoral condyles.
Patella
  Origin located at proximal pole
Tibia
  Origin at the midpoint of the femoral condyles with the knee in full extension

## Slide 4: Ligaments
patellar tendon
lateral collateral
popliteofibular
lateral bundle of posterior capsule
medial bundle of posterior capsule
oblique popliteal bundle of posterior capsule
arcuate popliteal bundle of posterior capsule
anteromedial bundle of anterior cruciate
posterolateral bundle of anterior cruciate
anterolateral bundle of posterior cruciate
posteromedial bundle of posterior cruciate
posterior bundle of superficial medial collateral
central bundle of superficial medial collateral
anterior bundle of superficial medial collateral
posterior bundle of deep medial collateral
anterior bundle of deep medial collateral
spherical wrapping surface for medial collateral

## Slide 5: Patellofemoral Joint

## Slide 6: How to run the passive flexion-extension test
Click to run ‘passiveFlexion_analysis.bat’
The results will be stored in the folder ‘Passive_Flexion’.
To analyze the data and plot results, run the function ‘passiveFlexionProcess.m’ in the ‘Matlab’ folder.

## Slide 7: Passive Flexion-Extension

## Slide 8: Passive Flexion-Extension

## Slide 9: Contact Model

## Slide 10: How to run the anterior-posterior stiffness test
Click to run ‘ap_analysis.cmd’
The results will be stored in the folder ‘AP_Laxity’.
To analyze the data and plot results, run the function ‘apLaxProcess.m’ in the ‘Matlab’ folder.

## Slide 11: Anterior-Posterior Stiffness

## Slide 12: Anterior-Posterior Stiffness

## Slide 13: Anterior-Posterior Stiffness

## Slide 14: Anterior-Posterior Stiffness

## Slide 15: How to run the axial rotation stiffness test
Click to run ‘ie_analysis.bat’
The results will be stored in the folder ‘IE_Laxity’.
To analyze the data and plot results, run the function ‘ieLaxProcess.m’ in the ‘Matlab’ folder.

## Slide 16: Axial Rotation Stiffness

## Slide 17: Axial Rotation Stiffness

## Slide 18: Axial Rotation Stiffness

## Slide 19: Axial Rotation Stiffness

## Slide 20: How to run the ab-adduction stiffness test
Click to run ‘vv_analysis.bat’
The results will be stored in the folder ‘VV_Laxity’.
To analyze the data and plot results, run the function ‘vvLaxProcess.m’ in the ‘Matlab’ folder.

## Slide 21: Ab-Adduction Stiffness

## Slide 22: Ab-Adduction Stiffness

## Slide 23: Ab-Adduction Stiffness

## Slide 24: Ab-Adduction Stiffness

## Slide 25: Ligament Properties

## Slide 26: Limitations
Model components come from different sources
  Bones: based on cadaveric study
  Muscle attachments: based on bone geometry
  Ligaments: based on bone geometry
  Femur for contact: based on OpenKnee MRI geometry
  Tibia for contact: simplified geometry
  Ligament properties: based on other models and tensile testing of cadaveric tissue
Model seems a little stiff. However, further loosening would cause more intercondylar lift-off during passive flexion-extension
Simplified patellofemoral joint and tibial geometry to increase computational speed
No scaling method…yet

## Slide 27: Summary
Why is this novel?
  First model like this that is open-source
Model is physiologically reasonable in passive motion, stiffness, ligament properties, and ligament function